## Slide 1
Design of Distributed Filter Based on Linear Matrix Inequality.
CPS Computational Learning Laboratory
1
Distributed Kalman filter for low obvservability
Distributed Kalman filter for sensor heterogeneity
Distributed Kalman filter with linear/nonlinear fusion estimation
Robust observer for external perturbations and nonlinear unmodeled dynamics
observer design for Predefined performance
①
②
③
④
⑤

## Slide 2
Distributed Kalman filter for low obvservability
Distributed Kalman filter for sensor heterogeneity
Distributed Kalman filter with linear/nonlinear fusion estimation
observer design for Predefined performance
Robust observer for external perturbations and nonlinear unmodeled dynamics
①
②
③
④
⑤
Information matrice
Deduce consensus gain

## Slide 3
Distributed Kalman Filter for Weighted
Directed Graphs
Published in: IEEE 58th Conference on Decision and Control (CDC)
Published Time: 2019
Paper 1
CPS Computational Learning Laboratory
3
Shiraz Khan , Raj Deshmukh , and Inseok Hwang

## Slide 4
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
CPS Computational Learning Laboratory
4
Notes: 主要分为以下四个部分

## Slide 5
CPS Computational Learning Laboratory
5
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 首先是问题描述

## Slide 6
Problem Description
Establishment of the structural framework of distributed Kalman filter in Weighted Directed Graphs
This study proposes an optimal distributed state estimation algorithm for weighted directed graphs to improved robustness and resilience of state estimation compared to KCF and the optimality of the state estimation is guaranteed.
Challenge
Estimation performance of distributed filters is susceptible to the communication environment.
The statement estimation solutions obtained are difficult to prove optimality.
Method
The optimal Kalman gain and optimal weight gain are obtained by taking the partial derivative of the trace of the covariance matrix.
CPS Computational Learning Laboratory
6

## Slide 7
CPS Computational Learning Laboratory
7
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 8
Method Design
①Define the posterior and prior estimate of the target state:
CPS Computational Learning Laboratory
8
②Define the posterior and prior estimate errors of the target state:
④Define the relevant symbols in this paper:
(1) is the Kalman consensus gain for sensor i.
(2) is the set of first-degree neighbors of sensor i.
③Define the cross covariance matrices of the estimation errors:

## Slide 9
Method Design
CPS Computational Learning Laboratory
9
But this estimation performance of this distributed filter is susceptible to the communication environment and the optimality of the solution is not guaranteed.
The parameter solvability condition that makes Eq. (7) solvable under the MMSE criterion is obtained as:
先验估计
新息
共识估计项

## Slide 10
Method Design
CPS Computational Learning Laboratory
10
Among them:
is the r-th element of the set
注：
表示各分布式滤波器的共识增益集合
表示对于分布式滤波器i，在i的邻居集中的
第r个分布式滤波器对i提供估计信息的贡献
表示在对分布式滤波器i计算后验状态估计时的总不确定度（先验协方差与观测噪声共同的影响）

## Slide 11
Method Design
CPS Computational Learning Laboratory
11
MMSE
criterion
Substituting the outer product terms with the corresponding covariance matrices：

## Slide 12
Method Design
CPS Computational Learning Laboratory
12
Partial derivative the trace of the a posteriori covariance matrix for eliminating the outer product

## Slide 13
Method Design
CPS Computational Learning Laboratory
13
注：相比于集中式kalman滤波器，分布式kalman滤波器的卡尔曼增益增加了由于共识滤波器引入的协方差矩阵，由此说明引入分布式滤波器有助于后验状态估计更加趋向于真值逼近。
Bringing Eq. (16) into Eq. (12) gives：

## Slide 14
Method Design
CPS Computational Learning Laboratory
14

## Slide 15
CPS Computational Learning Laboratory
15
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 16
Experiment Results
CPS Computational Learning Laboratory
16
A target moves in a circular path over a sensor network. The target is subject to system noise that causes its trajectory to be perturbed. The system with the following matrices:
Setting 1（Fully connected topology track）

## Slide 17
CPS Computational Learning Laboratory
17
Experiment Results
Setting 2
In this simulation, the sensor network has a chain topology (as presented in Fig. 4), in which there are 6 sensors connected in series. The sensors at either end (1 and 6) have only one first-degree neighbor (2 and 5, respectively)
We have performed 10,000 Monte Carlo simulations, and
in Fig. 5, the mean squared estimation error is plotted for：
（chain topology track）
Each sensor is locally observability

## Slide 18
2
CPS Computational Learning Laboratory
18
CPS Computational Learning Laboratory
18
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 19
Conclusion
①
②
CPS Computational Learning Laboratory
19
This paper design a weighted directed graph distributed Kalman filter algorithm,this algorithm not require any assumptions on the observability of the individual sensors.
This paper discussed the suboptimality in existing schemes and the validate the superior algorithm performance of the proposed scheme against the existing algorithms.

## Slide 20
Paper 2
CPS Computational Learning Laboratory
20
Publish Journal:IEEE Transections On Automatics Control(TAC)
Published Time: 2023
Optimal Kalman Filter With Information-Weighted Consensus
Shiraz Khan , Raj Deshmukh , and Inseok Hwang
Notes: 基于深度强化学习的柔性作业车间动态调度

## Slide 21
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
CPS Computational Learning Laboratory
21
Notes: 主要分为以下四个部分

## Slide 22
CPS Computational Learning Laboratory
22
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 首先是问题描述

## Slide 23
Problem Description
Distributed Kalman filter with heterogeneous sensors system
This study designed a distributed weighted consensus Kalman filter algorithm, this algorithm is able to achieve a directional flow of information in heterogeneous sensor networks. By incorporating consensus on a weighted directed graph (WDG), the proposed algorithm enables sensors to selectively assign higher weightage to accurate information and lower weightage to inaccurate or redundant information.
Challenge
How to assign the consensus weights in case of poor sensor performance (heterogeneous sensor networks scenario)?
Method
The derivation of optimal Kalman gain is achieved by minimizing the root-mean-square error, and the information matrix is used to measure the estimation performance of each sensor to derive the optimal weight gain.
CPS Computational Learning Laboratory
23

## Slide 24
CPS Computational Learning Laboratory
24
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 研究现状

## Slide 25
CPS Computational Learning Laboratory
25
Method Design
①Define the posterior and prior estimate of the target state:
②Define the posterior and prior estimate errors of the target state:
④Define the relevant symbols in this paper:
(1) is the Kalman consensus gain for sensor i.
(2) is the set of first-degree neighbors of sensor i.
③Define the cross covariance matrices of the estimation errors:

## Slide 26
CPS Computational Learning Laboratory
26
Method Design
Theorem 1: The distributed estimation algorithm following the update equation (5) minimizes the total mean-squared error (6) at each time step if and only if the following conditions are satisfied at all sensors in the network:
注：卡尔曼增益K代表滤波器更新机制，其只与优化准则有关，不与其他因素有关。
之后需要求解在异构传感器环境下的共识权值

## Slide 27
CPS Computational Learning Laboratory
27
Method Design
注：将分布式滤波器更新公式式（5）改写成式（9）的形式，为了后续推导选择传感器提供先验信息更重要的共识权重提供方便。
注：即协方差较小的传感器将具有较高的可靠性，将分配更高的权重。因此定义信息矩阵来衡量传感器性能的可靠性。

## Slide 28
CPS Computational Learning Laboratory
28
Method Design
注：式（14）代表总不确定性，包括观测噪声和各传感器引入先验协方差矩阵共同的影响。

## Slide 29
CPS Computational Learning Laboratory
29
Method Design
注：这里只考虑与传感器i有关的先验协方差，即只保留输入
传感器i的协方差矩阵

## Slide 30
CPS Computational Learning Laboratory
30
Method Design
式（20）代表此矩阵的特征向量为全1向量
之后需要求解式（21）中的

## Slide 31
CPS Computational Learning Laboratory
31
Method Design
注：利用先前推导的与协方差无关的卡尔曼增益表达式作为已知条件，将 解出。

## Slide 32
CPS Computational Learning Laboratory
32
Method Design
The estimation error covariance can be obtained by substituting (9), (28), and (29) into (3), as

## Slide 33
CPS Computational Learning Laboratory
33
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 34
Experiment Results
CPS Computational Learning Laboratory
34
In this section, the Optimal KCF-WDG algorithm is validated and its estimation performance is compared against those of existing algorithms through an illustrative numerical simulation. We consider the problem of target tracking using a network of cameras, which is an example of a distributed estimation scenario.
The process noise covariance
The initial value of
the state vector is
The FoV of each camera (depicted by the yellow shaded region) is a triangle with an apex angle of 70◦ and height of 70 m, such that the apex of the triangle lies on the sensor.

## Slide 35
Experiment Results
CPS Computational Learning Laboratory
35

## Slide 36
2
CPS Computational Learning Laboratory
18
CPS Computational Learning Laboratory
36
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 37
Future Work
Contributions
In this article, a novel distributed estimation algorithm has been proposed, which extends the KCF to incorporate weighted consensus. the estimation gains of OKCF-WDG were optimized at each sensor to achieve the minimum mean-squared error in the heterogeneous sensor networks distributed setting.
CPS Computational Learning Laboratory
37
Future Work
The future work on OKCF-WDG would look into formalizing the estimation of the distributed information matrix such that it can be estimated efficiently in terms of computing and communication costs. A formal stability analysis of the algorithm will also be conducted.

## Slide 38
A New Approach to Linear/Nonlinear Distributed
Fusion Estimation Problem
Paper 3
CPS Computational Learning Laboratory
38
Bo Chen ,Guoqiang Hu , Daniel W.C. Ho , and Li Yu
Publish Journal:IEEE Transections On Automatics Control(TAC)
Published Time: 2024

## Slide 39
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
CPS Computational Learning Laboratory
39
Notes: 主要分为以下四个部分

## Slide 40
CPS Computational Learning Laboratory
40
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 41
Problem Description
Collaborative multi-view IB for flexible unsupervised representation learning
In this paper, we study the distributed fusion estimation problem for linear time-varying systems and nonlinear systems with bounded noises.
Challenge
the disturbance noises in practical systems are always bounded, and the statistical property of noises is difficult to be accurately obtained in practical applications.
Method
The novel constructive proposed to find an upper bound of fusion estimation error, then a convex optimization problem on the design of an optimal weighting fusion criterion is established in terms of linear matrix inequalities, which can be solved by standard software packages.
CPS Computational Learning Laboratory
41

## Slide 42
CPS Computational Learning Laboratory
42
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 研究现状

## Slide 43
Method Design
CPS Computational Learning Laboratory
43
is the system state;
is the measured output from sensor i;
are time-varying bounded matrices.
Among them:
satisfied:
L is the number of sensors
Nonlinear system dynasic model:
注：针对一般情况的白噪声，满足：
即能量函数无界。本论文考虑在有界情况的噪声（非白噪声）下的状态估计问题。

## Slide 44
Method Design
CPS Computational Learning Laboratory
44
Local state estimator(LSE):
denotes one-step prediction;
Among them:
denotes optimal gains;
注：将非线性系统局部线性化，化简为近似扩展卡尔曼滤波器的形式

## Slide 45
Method Design
CPS Computational Learning Laboratory
45
Distributed fusion estimate(DFE):
注：
（1）首先需要设计最优增益K，使得平方根误差存在上界；
（2）之后需要设计权重增益，使最小化SE的值。

## Slide 46
Method Design
CPS Computational Learning Laboratory
46
①DFE Design for Linear Time-Varying Systems
Before deriving the result of Theorem 1, define:
注：式（11）为保证平方根误差有界的最优增益K求解方法；
式（13）为保证平方根误差最小化的权重参数求解方法。

## Slide 47
Method Design
CPS Computational Learning Laboratory
47

## Slide 48
Method Design
CPS Computational Learning Laboratory
48
证明平方根误差有界

## Slide 49
Method Design
CPS Computational Learning Laboratory
49
证明平方根误差最小化的优化目标
需利用schur补引理确保将此线性矩阵不等式转化为计算机可解的形式

## Slide 50
Method Design
CPS Computational Learning Laboratory
50

## Slide 51
Method Design
CPS Computational Learning Laboratory
51
②DFE Design for Linear Time-Varying Systems
注：将问题拓展到非线性系统，用扩展卡尔曼滤波的方式将非线性系统在平衡点处局部线性化。

## Slide 52
Method Design
CPS Computational Learning Laboratory
52
注：式（28）为保证平方根误差有界的最优增益K求解方法；
式（30）为保证平方根误差最小化的权重参数求解方法。

## Slide 53
Method Design
CPS Computational Learning Laboratory
53
注：此证明过程与线性时变系统类似。

## Slide 54
Method Design
CPS Computational Learning Laboratory
54
Solved by the function “mincx” of MATLAB LMI Toolbox

## Slide 55
CPS Computational Learning Laboratory
55
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 56
Experiment Results
CPS Computational Learning Laboratory
56
A. Target Tracking System

## Slide 57
Experiment Results
CPS Computational Learning Laboratory
57
Under the Type I, SEs of the H∞ filter and the LSE in this paper.
Under the Type II, Ses of the Kalman filter and the LSE in this paper.
Under the Type II, PMSEs of the LSE in this paper and the Kalman filters with knowncovariances and unknown covariances.
Under the Type III,SEs of the LSE in [21], and the LSE in this paper.

## Slide 58
2
CPS Computational Learning Laboratory
18
CPS Computational Learning Laboratory
58
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 59
Future Work
Contributions
1.For the linear time-varying systems, a new stable local Kalman like estimator, is obtained by solving a convex optimization problem at each time step. Subsequently, by constructing a new upper bound of fusion estimation error, an optimal distributed fusion criterion is designed by solving a class of convex optimization problems.
CPS Computational Learning Laboratory
59
Future Work
when considering the communication uncertainties including bandwidth constraints, transmission delays and packet dropouts, one of our future works will focus on how to design the networked nonlinear fusion estimation algorithms based on the developed fusion estimation method in this paper.
2.Linearizing the nonlinear function using Taylor series expansion, and the linearized errors can be viewed as bounded noises. According to the design method of linear time-varying fusion systems, each local nonlinear estimator and a distributed fusion criterion are designed by establishing different convex optimization problems.

## Slide 60
Dynamical robust H-infinite filtering for nonlinear
uncertain systems: An LMI approach
Masoud Abbaszadeha, Horacio J. Marquez
Paper 4
CPS Computational Learning Laboratory
60
Published in:Journel of the Franklin Institute
Published Time: 2012

## Slide 61
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
CPS Computational Learning Laboratory
61
Notes: 主要分为以下四个部分

## Slide 62
CPS Computational Learning Laboratory
62
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 首先是问题描述

## Slide 63
Problem Description
bserver design for prespecified decay rate convergence with LMI method
This paper consider a prespecified decay rate guaranteeing the exponential convergence of the estimations. In addition, when the static-gain observer also exists,the maximum admissible Lipschitz constant obtained using the proposed dynamical observer structure can be much larger than that of the static-gain observer. The achieved observer guarantees asymptotic stability of the error dynamics with a prespecified decay rate (exponential convergence)
Method
this paper have propose an LMI approach to nonlinear filtering in which the Lipschitz constant is one of the LMI variables in order to achieve a maximized admissible Lipschitz constant through convex optimization for systems with uncertainties in linear and nonlinear parts of the state space realization.
CPS Computational Learning Laboratory
63

## Slide 64
CPS Computational Learning Laboratory
64
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 研究现状

## Slide 65
Method Design
CPS Computational Learning Laboratory
65
注：满足lipschiz条件的函数的在某方向上斜率均不大于其方向上的lipschiz常数
（1）continuous-time uncertain nonlinear systems
Notes: 图1给出了所提出的HMAPPO在不同时空水平上的总体操作机制。objective agent充当周期性地调整较高目标的较高控制器。作业智能体和机器智能体是底层执行者，在每个重调度点分别选择可行的作业选择规则和机器分配规则，以达到更高的目标。

## Slide 66
Method Design
CPS Computational Learning Laboratory
66
（1）continuous-time uncertain nonlinear systems

## Slide 67
Method Design
CPS Computational Learning Laboratory
67
（2）Observer structure
注：式（10）建立为带状态反馈的龙伯格观测器形式

## Slide 68
Method Design
CPS Computational Learning Laboratory
68
注：将式(2)和式(9)代入(13)中，得到观测器误差传递方程(14),(15)

## Slide 69
Method Design
CPS Computational Learning Laboratory
69
Prove observer error dynamics lipschitz property
注：矩阵的L2范数计算：

## Slide 70
Method Design
CPS Computational Learning Laboratory
70
Disturbance attenuation level and guaranteed decay rate
之后需要利用lyapunov方程建立满足上式成立下lipschitz常数的上界
satisfied

## Slide 71
Method Design
CPS Computational Learning Laboratory
71
observer synthesis

## Slide 72
Method Design
CPS Computational Learning Laboratory
72
注：通过式（29）保证性能

## Slide 73
Method Design
CPS Computational Learning Laboratory
73
注：对于式（33）而言，需要分为两部分对式子进行放缩，从而找到上界。

## Slide 74
Method Design
CPS Computational Learning Laboratory
74
注：通过添加变量表示更加直接，且防止在定理1求解凸优化问题时对过定义。
①
注：利用矩阵分解方法，并构造引理2的形式，使得矩阵可以化为对称二次型形式，方便后续schur补引理化简为LMI形式

## Slide 75
Method Design
CPS Computational Learning Laboratory
75
For:
利用式①对下式黄色部分进行放缩：
利用lamma1和lamma2对蓝色部分进行放缩，即：

## Slide 76
Method Design
CPS Computational Learning Laboratory
76
由此可得：

## Slide 77
Method Design
CPS Computational Learning Laboratory
77
satisfied
对于：
Define Lyapunov function
Derivation with respect to time
注：为使系统按衰减速率收敛，则需保证lyapunov函数满足 。
Solving following differential equations
①
②

## Slide 78
Method Design
CPS Computational Learning Laboratory
78
联立式①②，得：
①
②
针对先前推导的误差动力学方程（15）,有：

## Slide 79
Method Design
CPS Computational Learning Laboratory
79
注：式（42）保证了误差方程e(t)具有衰减率动态过程

## Slide 80
Method Design
CPS Computational Learning Laboratory
80
Schur complements lamma：
define：
Schur lamma
define：
Schur lamma
define：

## Slide 81
Method Design
CPS Computational Learning Laboratory
81
将式（39）通过schur补转化为LMI形式，得到式（43）：
其中：
对于nominal system,其w=0。

## Slide 82
Method Design
CPS Computational Learning Laboratory
82

## Slide 83
Method Design
CPS Computational Learning Laboratory
83
Robustness against nonlinear uncertainty

## Slide 84
CPS Computational Learning Laboratory
84
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 85
Experiment Results
CPS Computational Learning Laboratory
85
注：可以看到本论文使用的观测器设计方法的容许lipschitz常数相比之前研究有明显增加，即说明设计的观测器的保守性有所降低，且具有渐进鲁棒性。

## Slide 86
2
CPS Computational Learning Laboratory
18
CPS Computational Learning Laboratory
86
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 87
Future Work
Contributions
This paper consider a prespecified decay rate guaranteeing the exponential convergence of the estimations. It will be shown that the proposed dynamical structure has additional degrees of freedom when compared to theconventional static-gain observers and is capable of robustly stabilizing the observer error dynamics for some of those systems for which a static-gain observer cannot be found.
CPS Computational Learning Laboratory
87
In addition, when the static-gain observer also exists,the maximum admissible Lipschitz constant obtained using the proposed dynamical observer structure can be much larger than that of the static-gain observer. The achieved observer guarantees asymptotic stability of the error dynamics with a prespecified decay rate (exponential convergence)

## Slide 88
An LMI-Based Robust Nonlinear Adaptive Observer for Disturbed Regression Models
Paper 5
CPS Computational Learning Laboratory
88
Héctor Ríos , Alejandra Ferreira de Loza , Denis Efimov and Roberto Franco
Publish Journal:IEEE Transections On Automatics Control(TAC)
Published Time: 2024

## Slide 89
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
CPS Computational Learning Laboratory
89
Notes: 主要分为以下四个部分

## Slide 90
CPS Computational Learning Laboratory
90
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 首先是问题描述

## Slide 91
Problem Description
Robust LMI method for disturbed regression models observer design
This paper contributes with an adaptive observer for a class of disturbed dynamical regression models and algorithm deals with the time-varying parameter identification problem.
Challenge
Any parameter identification procedure relevant to real applications must deal with disturbances comprising time-dependent perturbations and disregarded dynamics.
Method
The gain tuning of the algorithm is constructive, and it is based on the solution of a set of LMIs. And through LMI method
making the Lyapunov equation negative definite.
CPS Computational Learning Laboratory
91
Notes: 任何与实际应用相关的参数识别过程都必须处理包含与时间相关的扰动和忽略动力学的扰动

## Slide 92
CPS Computational Learning Laboratory
92
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design
Notes: 研究现状

## Slide 93
Method Design
CPS Computational Learning Laboratory
93
Problem statement:
Assumtion:
(1)
(2)
(3)
(4)
is the output available for measurement
is a continuous function of time, which is measurable
is the vector of unknown time-varying parameters
represents unmeasurable disturbances comprising time
(5)
w is locally Lipschitz continuous function of y and piecewise continuous in t
(6)
注：对于状态不可完全观测系统，系统参数数量大于可用于测量的状态数，即p>m ,因此需要假设可测输出和不确定参数相关性质。
dependent external perturbations and nonlinear unmodeled dynamics
在存在依赖于时间的外部扰动和非线性未建模动力学，需要使用可测输出y和回归向量Γ识别时间变化参数θ的向量
Notes: 表示由时间相关的外部扰动组成的非线性扰动和非线性非建模动力学

## Slide 94
Method Design
CPS Computational Learning Laboratory
94
Robust Nonlinear Adaptive Observer:
is the estimation output y
is the estimation output error
define the function
Assumtion:
(1)
(2)
(3)
(4)
(5)
and β > 1
(6)
注：将式（1）中的动力学模型带入自适应观测器中，得到误差动力学方程，因此只需对此方程的稳定性和收敛性进行分析。
Notes: 扰动的影响出现在状态估计误差动力学中，而参数变化的影响出现在参数识别误差方程中。

## Slide 95
Method Design
CPS Computational Learning Laboratory
95
The disturbance terms
are compensated by the observer terms
假设2引入输出y的不同次幂和范数相关的项，以及一个非负常数项w。明确扰动的可处理性，同时涵盖了多类型的扰动（大扰动、小扰动、随机扰动）。
之后证明自适应观测器在扰动满足假设2下的稳定性和收敛性
Notes: 上界也考虑了不消失的时变外部扰动，它以w+为界。因此，假设2对大量的扰动都是有效的。

## Slide 96
Method Design
CPS Computational Learning Laboratory
96

## Slide 97
Method Design
CPS Computational Learning Laboratory
97

## Slide 98
Method Design
CPS Computational Learning Laboratory
98

## Slide 99
Method Design
CPS Computational Learning Laboratory
99

## Slide 100
Method Design
CPS Computational Learning Laboratory
100

## Slide 101
CPS Computational Learning Laboratory
101
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 102
Experiment Results
CPS Computational Learning Laboratory
102
The solution to the given LMIs is obtained by means of SDPT3 solver, among YALMIP in MATLAB.
(1)The time-varying parameters satisfy Assumption 1:
(2)Follow the Algorithm 1 to compute the observer parameters:
(3)Follow the LMI parameters:

## Slide 103
Experiment Results
CPS Computational Learning Laboratory
103
(3)Follow the LMI parameters:
(4)Consider the initial conditions

## Slide 104
Experiment Results
CPS Computational Learning Laboratory
104

## Slide 105
2
CPS Computational Learning Laboratory
18
CPS Computational Learning Laboratory
105
Contents
Problem Description
01
03
Experiment Results
04
Conclusion
02
Method Design

## Slide 106
Future Work
Contributions
1.This algorithm counteracts the effects of the disturbances comprising time-dependent external perturbations and
nonlinear unmodeled dynamics;
2. The parameter identification error converges asymptotically to a region around the origin, which can be made acceptably small by a proper tuning of design parameters;
3. The gains synthesis of the algorithm is constructive since it is based on the solution of a set of linear matrix inequalities (LMIs).
CPS Computational Learning Laboratory
106

## Slide 107
Thank you for listening